## Slide 1: TDR Wheels

## Slide 2: 1 - Input : Frame
The robot needs to evolve on vinyl
According to the structural plans (see TDR structure) three different sets of wheels are needed
  motor wheels : transmit power
  coding wheels : need for punctual contact
  rotules : stabilisation

## Slide 3: 1 - Input : Motor wheels
The motoreducer has an output diameter of 4mm
Dimensioning of motors has been done with 4 cm radius wheels they thus shall not be smaller

## Slide 4: 1 - Input : Coding wheels
The rotary encoder has
  an output diameter of 6mm
  a 15mm long shaft and the wheel shall not be wider to ensure compactness
  an overall diameter of 38mm
Contact needs to be as punctual as possible

## Slide 5: 1 - Input : Rotules
The rotules need not to hinder movement
Rotules needs to allow the robot to be horizontal

## Slide 6: 2 - Analysis : motor wheels
In phases of acceleration and braking, the robot needs not to slide. The motor wheels should then :
  have the biggest surface of contact possible with the floor
  have no real need for precision for the retro control will be estimated with independent encoding wheels
The hole needs to be at least 4mm wide, if it is really larger, an adaptor can be used
The choosing of the wheel is more than in many other cases influenced by what exists in the market

## Slide 7: 2 - Analysis : Coding wheels
The bet of splitting motricity and encoding can only be won if the coding wheels are
  small enough
  always in contact with the floor
To ensure a minimum play, the best solution is to connect directly the wheel to the encoder
  The wheel shall then at least be larger than the overall encoder diameter (38mm)
  The connection between the wheel and the encoder needs to be very tight

## Slide 8: 2 - Analysis : Rotules
They shall stabilize the robot.
The rotules must help during movement.
Two are necessary : front and back of the robot (see TDR structure), to ensure that the frame does not touch the floor.

## Slide 9: 3 - Choice of structure : motor wheels
We chose to go with 2’’ (5cm) wheels with outer thread in TPU
Paired with an adaptor to fit the shaft diameter
It is quite difficult to assess the quality of a wheel and if it will connect well with the motor the wheels
  The wheels could well be changed during the design

## Slide 10: 3 - Choice of structure : encoding wheels
No commercial wheels fitted our needs
Our tutor explained us that it was not out of reach to manufacture in the surroundings laboratories
  aluminium manufactured 20mm radius
  contact by an O-ring to ensure punctuality

## Slide 11: 3 - Choice of structure : rotules
According to the previous analysis, we chose to use a small metallic rotule
Which height could be adapted.

## Slide 12: 4 - Conclusion
The motor wheels are commercial ones and only need to be efficient which will be more or less assessed empirically
Coding wheels need to comply with very precise specifications and will then be manufactured on purpose
Rotules are not a crucial point and can be adapted empirically like the motor wheels