## Slide 1: TDR Observation
Giving eyes to the machine

## Slide 2: Objective
Make the Robot able to know where he is and to spot the opponent and the atoms

## Slide 3: 1 - Input
The Robot shall know its position and orientation
The position of the opponents, up to two, shall be available
The Robot shall know if the actions he attemps to make are successful
The Robot shall know where the atoms are and what there colors are

## Slide 4: 2 - Analysis
The cup has a very particular context : the operating space is limited and known, which means only a few specific objects need to be detected : the robots and the atoms. Thus there is no need to compute the entire environment.
The place of the cup is also subject to a lot of noise : autofocus of cameras, high density of wave-emitting devices, sensors of the other robot.

## Slide 5: 2 - Analysis : Sensors types
Lidar : high resolution, gives position and speed, expensive
Radar : gives position and speed, medium resolution
Sonar : low cost, best for close range, susceptible to noise
Camera : gives position and color, low cost, data easy to comprehend

## Slide 6: 3 - Choice : The camera
We decided to use a camera because of the possibilities to detect colors and because we were more familiar with the technology. It also exploits the mast on the side of the table which offers a perfect vantage point.

## Slide 7: 3 - Choice : Field of view
The camera must be able to see the whole table with a sufficient resolution. Considering the size of the table, we need at least a field of view of 107°.
Therefore, we chose a Raspberry Pi camera with a fisheye lens : it offers a FOV of 160° with a resolution of 2592×1944, in exchange for a deformation of the image which can be corrected by an algorithm.

## Slide 8: 3 - Choice : Image processing
To compute the image and obtain the coordinates of robots and atoms, we chose a Raspberry Pi powered with a power bank.
Image-processing tools already exist on Raspbian, which means we can adapt pre existing algorithms instead of starting from scrap.
Moreover, computing the position before sending the data to the robot is a mean to reduce the charge on the robot’s processor, which can focus on other tasks.

## Slide 9: 3 - Choice : Communication
The two solutions that seemed appropriate are WiFi and Bluetooth, since everything else (IR, radio waves, RJ45 cable…) are either forbidden or subject to important perturbations.
We went for WiFi, as it is the main choice for many Raspberry users. That means we can benefit from the community and use already developped protocols.
The Raspberry Pi has a built-in WiFi module, and it is easy to set up a network and have the robot and the system connect to it on boot.

## Slide 10: 4 - Conclusion
We are going to use a camera connected to a Raspberry Pi in order to recognize atoms, verify points and locate the robots.
It will take a photo, analyse it and send it to the robot at a constant frequency (max 500ms). It also means that we can get a position from a moving object with the same precision as a standing object, as long as the photo is clear.
The system and the robot will communicate using WiFi.